Hello everyone I am Khritish, my project is on energy effiecient neuromorphic computing, and Dr. Kuntal Roy is advisor

---
This is my content slide, where I will Recap what I have done in mid term, than I will talk about the simulation I have performed, then how to make neural network using spintronics, then I will talk about the experiments I have performed and atlast the future plans

---
Now I will recap of what i had presented in my id term

---
Neuromorphic comptuing is generally performed on traditianal transistor based devices
In my project, I’ll be using spintronics based devices
There are few inherent advantages of using spintronic devices such as weight, sum threshold function comes inbuilt and the non-volatility nature of spintronics device
There will be non-boolean computing

---
ANN is a system of interconnected neurons
Where one neuron in a layer is connected to all other neuron in the next layer
Mainly there are three layers in NN,
Input layer, where the input is given,
Output layer, where the output is recived, and the
hidden layer, where the internal computation of the NN happens
Edges connecting nodes have a weight and each node has a bias term
Here I correlate the biological neuron with artificial neuron, the dendrites are input, soma is equivalent to Summation and activation and the axon is the output

---
Here is an implementation of a character recognition model
Where we provide a 35 bit word, noisy pixel value of a 7x5 character, into the fully trained model, and the model predicts 26 bit word, suggesting the output

---
Now I will talk about magnetic anisotropy, which means magnetization is not same in all the direction, and hence the energy
In case of a sphere, there is no anisotropy
But in case of an ellipsoid, we have anisotropy but it is difficult to fabricate on a planar wafer
Hence we use a elliptical cylinder, which has in-plane shape anisotropy
We have different energy at different values of theta,
Here the Energy is minimum, when theta = 0 or 180, also at theta theta = 90, we have a energy barrier, which prevents the spontaneous fluctuation of spin
Here the Hk is the coercive field
Generally, the Energy barrier, kept in between 30 to 80 KT, and at 40 KT the data retention time is 10 years

---
Now I will talk about simulation

---
In this slide we demonstrate, the effect on magnetization rotation on application of magnetic field along in-plane hard axis
We have applied the magnetic field in the Y-axis
Below I have plot of Energy vs theta, where the energy is given by this equation
And the magnetization will attain equilibrium, at those theta where the energy is minimum
So by computing dE/dtheta=0, we get theta_min=sin-1(Hy/Hk)
[CLICK]
When Hy/Hk =0, we have this curve, where theta_min= 0 or 180, magnetization can’t spontaneously flip, because there is potential hill ahead
[CLICK]
Now when Hy/Hk=0.7, theta_min is shifted to 45 or 135 degree,
CLICK
If we make Hy/Hk=1, theta_min becomes 90,
CLICK
On further increasing the Hy/Hk value, the energy will decrease further but theta_min will be 90
Hence we conclude that, we can’t rotate the spin by applying magnetic field along in-plane hard axis

---
Now if we apply, magnetic field along in-plane easy axis, that is along z axis
theta_min will be given by sin-1(Hz/Hk)
Here I have plotted energy vs theta
CLICK
When Hz/Hk=0, theta_min = 0 degree
CLICK
When Hz/Hk=1, theta_min=90 degree
CLICK
And when Hz/Hk=1.4, theta_min=180 degree
Which means we have fliped our magnetization,
Now on slowly removing the externally applied magnetic filed, we see there is a potential up hill from theta = 180 to theta = 0, hence even after removing the magnetic field, the magnetization does not comes back to the original
So form this we conclude that, we can rotate the magnetization on application of magnetic field along in plane easy axis

---
In this slide I will explain the perpendicular anisotropy, that is here the magnetization is perpendicular to planar surface,
The need of perpendicular anisotropy, so that we can work with smaller cross section area, its like transistor scalling,
There are two possiblities of perpendicular anisotropy, bulk and interface
Here energy is given by the equation
CLICK
Where nd_teta_phi is given by this eqn...which is in spherical cordinates
Using Hd and Hk in the above equation we get, E shape as this equation
CLICK
Due to circular cross section, Hd=0, hence in E_shape the phi term vanishes, but it is only true when we have circular crossection
Substituting Hpm=Hk+H_interface in Epma we get this equation

---
This are experimental curves, when thicknes of CoFeN is 2nm, we observe hystereisi in in-plane, and do-not observe any hysterisis in out of plane
But when thickness of CoFeB is 1.3nm the curves switches
That is when the thickness is less than 1.3nm interfacial anisotropy dominates
And when the thickness is more than 1.3nm bulk anisotropy dominates

---
Now I will talk about Neural Network using spintronics

---
In this slide we will talk about Multiferroics and multiferroic composites
In nature there exist, ferroelectric and ferromagnetic materials, there also exist multiferroic, which exhibit both the properties of FE and FM, that is change in Electric field, will change the magnetization and change in magnetic field will change the polarization
In the figure below, the E, H, and the stress are the physical parameters which we can change , and the P, M, and strain are the macroscopic observables
So we use a multiferroic composite, its the composition of Piezoelectric and magnetostrictive material
The magnetoelectric coupling is given by alpha_ME
Multiferroic composites are stress mediated

---
In the previous slide, we talked about multiferroic composites, where we used magnetostrictive
So magnetostrictive materials are FM specimens, which changes its shape during the process of magnetization
The magnetic anisotropy creates to stress anisotropy, and vice versa
The stress anisotropy generated is given by the equation 3/2lambda...
Where lambda is the magnetostriction coefficient, which is the saturation strain generated on application of magnetic field
The 3/2 lambda values of Cobalt is -30 x 10-6 and Iron-Gallium is 150 x 10-6

---
Here we have the multiferroic composite, and we apply electric potential to the piezoelectric, which will create strain in the piezoelectric
The strain is given by the formula epsilon_piezo.....
The strain will be elastically transferred to the magnetostrictive material
From that we calculate the stress anisotropy
And for FeGa the stress anisotropy is 2.4 x 10-18 J

---
This is my proposed device, here I will explain, how my device will simulate the artificial neuron
When electric voltage is given to piezoelectric, it stresses the piezo, the stress is elestiaclly transfered to the magnetostrictive material
Stress anisotropy in magnetostrictive creates magnetic anisotropy
Which changes the magnetization direction in the TMR
And this gives variable voltage as output

---
Now I will talk about the experiment I have preformed and experimental setups i have learned

---
Now I will explain on Magnetic Thermal Annealing
The lattice and shape deformities in materials can significantly degrade its quality
Removing the anomalies is necessary to achieve a high quality material and performance
A common technique is thermal annealing, which is done by raising, maintaing and slowly reducing the temperature of the material
[click]
This allows, atoms inside of the material to diffuse more easily to find their proper location, and maintaining the material at high temperature, lets it achieve equilibrium, eliminating structural imperfection
[CLICK]
In Magnetic Thermal Annealing
The difference is ext. Magnetic field is applied during the annealing process

---
The most important effect of MTA, in FM material is that it re-orients the easy axis or the axis of the spontaneous magnetization vector
[click]
If a lattice shows specific symmetry, the easy axis will normally reflect the symmetry
[click]
Now if a lattice has more deformities, then there won’t be any major global symmetry, which will weekend the magnetization vector
[click]
If a deformed FM, annealed at higher temperature, all the spins of each individual atom will align with the ext. Applied field
And the temperautre is reduced, the lattice becomes locked, and the magnet attains a new magnetization direction

---
This is the Magnetic Thermal annealing setup in our lab
Where we have heater, which can go upto 500 deg C
This heating chamber is connected to the vacuum pump, which create vaccum during the annealing process
We have electro magnet, which provides constant magnetic field, which is connected to the chiller, which cools down the electromagnet
The constant current power supply, controls magnetic field generated by the electromagnet
At the bottom there is the sample holder, it can be rotated 360 degree, to in-plane or perpendicular magneization

---
This is my experimental result for Magnetic Thermal Annealing
Where I have taken a CoFeB of 10nm thickness
This is the magnetization curve generated from the VSM,
VSM stands for Vibrating Sample Magnotometer, which is used for magnetic characterization of samples, since I don’t have access to the VSM, it was done by one of the PhD student at our lab
The sample was maintained at 400 deg C for 1 Hr, in presence of 400mT magnetic field in the direction of in-plane easy axis
In the figure the blue curve shows the , magnetization curve before the magnetic thermal annealing, whose coercive field is 21 Oe, and total magnetization is 3.7 x 10-5 emu
And the red curve shows the magnetization curve after the magnetic thermal annealing, whose coercive field is 70 OE, AND Magnetic Saturation is 5.2 x 10-5
After magnetic thermal annealing the saturation magnetization is 1.43T
We can see that there is a significant increase M-H area, the red curve area is 18.5 times more then the blue one

---
This are instruments I have learned,
Spin coater for thin film deposition on wafers
Shaker to shake solutions
Hot plate to bake samples
Ultrasonic cleaner for to clean beaker, by use of ultrasonic frequency

---
Hot air oven, for thermal annealing, it can go upto 250 deg C
Rota mantle for heating up solutions while stiring using a magnetic stirer
Then Nitrogen gun and cyliner to clean very thin wafer using N2 gas, pipes are connected all over the lab to transport the N2 gas

---
Vacuum desiccator to put sample in vacuum, a vacuum pump is connected to it create vacuum
Muffle furnace for thermal annealing, it can reach upto 1200 deg C
And fumehood, to perform reactions, which can toxic, or irritating fumes, it can also prevent from spillage of dangerous acids

---
CLICK
Kethley Source meter for IV characterization, its is four quadrant device, it can used as source, that it can deliver power to the load and as a sink, where it will dissipate power
CLICK
Rohde and schwarz Power supply for IV characterization, its a two quadrant device, it can only be used source

---
Probe station is for IV characterization of very thin samples, where there is a micro-positioner it makes contact with the sample, and it is connected to the SMU or power station to deliver power
Here there is IV charatericts of diode performed using probe station
Then we have the oscilloscope, for visulaization of signal

---
Labview is a graphical programming environment, for automated reaserch, validation and production test systems
We will use to control and synchronize different device

---
Here I have made a labview program that can use one channel of power supply as stepper and the second channel as a sweep

---
The main application of the power supply is t create the IV charateristics of MOS S170 mosfet, the gate voltage was steep from 1.2 to 1.6v with steep of 0.1, and the drain voltage was sweep from 0 to 5 v, with steep of 0.1
The other are the resistance and diode characertistics

---
This is the labview program, for sweeping the SMU from 2 different voltage

---
Here also I have computed the IV characteristics of MOS S170, 1k ohm resistance and a diode

---
Introduces yourself

---
Introduces yourself