## Slide 1: Spintronics: Spin-Electronics
Electron
Along with charge, electrons have spin
Spin Up (↑) / Down (↓)
Spintronic devices are non-volatile and endurable
Advantage over transistors (requires extra circuitry )
There is no charge movement, only spin rotation
No ohmic energy dissipation
There is dissipation due to magnetization damping
There is dissipation due to applying charge voltage/current
Charge
Spin
0 / 1
Spin
Electron beam lithography (EBL)
A rapidly developing nanotechnology

## Slide 2: Giant Magneto-Resistance (GMR)
A. Fert, M.N Baibich et al., Phys. Rev. Lett. 61, 2472 (1988)
P. Grunberg, G. Binash et al., Phys. Rev. B 39, 4828 (1989)
Giant Magneto-Resistance (GMR)
1988
Notes: Magneto resistance: With the effect of magnetic field, how resistance get changed.

## Slide 3: Tunneling magneto-resistance (TMR)
Conductance is proportional to the density of states
NL↑, NR↑, NL↓, NR↓
Julliere, M. Tunneling between ferromagnetic film. Phys. Lett. A 54, 225-226 (1975)
Moodera, J. S. et al., Phys. Rev. Lett. 74, 3273 (1995)
Mathon, J. et al., Phys. Rev. B 63, 220403 (2001), Butler, W. et al., Phys. Rev. B 63, 054416 (2001)
Yuasa, S. et al., Nature Mater. 3, 868 (2004), Parkin, S. et al., Nature Mater. 3, 862-867 (2004)
Reported 1975 (prior to GMR)
TMR>500% using MgO spacer
Insulator
e.g., Al2O3, MgO
Left (L)
Right (R)
Left (L)
Right (R)

## Slide 4: Multiferroics and Multiferroic Composites
Piezoelectric
Strain
Magnetostrictive
P
E
H
M
Piezoelectricity
Magnetostriction
Magnetoelectricity (intrinsic)
P
E
H
M
Piezoelectricity
Magnetostriction
Magnetoelectricity (intrinsic)
Multiferroic
Notes: Change it to multiferroic composites

## Slide 5: Multiferroic composites Voltage vs stress anisotropy
Vin
tpiezo
Y: Young’s modulus
strain transfer
Piezoelectric
Magnetostrictive
z (3)
x (1)
tmag
y (2)
Magnetostrictive layer
with high
Choose piezoelectric layer with high de-coefficient