## Slide 1: Spintronics: Spin-Electronics
Spin
Electron
Charge
Apart from having charge, an electron has spin
Up/Down 0/1 (binary information)
E barrier
A rapidly developing nanotechnology
  Store, non-volatile
  Process
  Communicate
  In-built functionality
No charge movement, rotation of spin
  No ohmic dissipation, but dissipation due to damping
There is dissipation due to applying charge voltage/current
Key Issue
Notes: Spin is the intrinsic angular momentum of an elementary particle as being the result of its rotation about its own axis
In Spintronics, information is stored and transmitted using another property of electrons called spin.
Electrons moving through a nonmagnetic material normally have random spins, so the net effect is zero. External magnetic fields can be applied so that the spins are aligned (all up or all down), allowing a new way to store binary data in the form of one’s (all spins up) and zeroes (all spins down).

## Slide 2: Single-domain nanomagnets
W.F. Brown Jr.,
The fundamental theorem of the ferromagnetic particle theory
Magnetic domain formation should be limited to very small dimensions (100 nm) because of the competition between the magnetostatic energy and the quantum-mechanical exchange energy, causing nanomagnets to behave like single giant spins.
Electron beam lithography (EBL)
Exchange interaction
  Pauli’s exclusion principle
  Coulomb repulsion
Each electron small magnet
  Ferromagnet
  Ferrimagnet
  Antiferromagnet
Notes: Single domain nanomagnets are formed due to exchange interaction, which is a simultaneous action of Pauli’s exclusion principle and Coulomb repulsion.

## Slide 3: Magnetic anisotropy
: Coercive field
: Volume
In-plane
Shape anisotropy
Perpendicular anisotropy
CoCrPt
Bulk
tCoFeB<1.3 nm
CoFeB
MgO
Interface
M
H
Hk
z
y
Magnetization
x
30-80 KT at 300 K
CoFeB
Ellipsoid
Sphere
Notes: If volume increases then E barrier also increases, because of that spontaneous fluctuation minimizes.
id demagnetization factor
If volume increases then E barrier also increases, because of that spontaneous fluctuation minimizes.
𝑁_(𝑑−𝑦𝑦) id demagnetization factor

## Slide 4: Magnetization dynamics Landau-Lifshitz (LL) equation
precession
damping
M= Magnetization
E= Potential energy
=Volume
Performance metrics
Phenomenological
damping parameter
Switching delay and energy dissipation
Damping causes a transfer of energy from macroscopic motion to microscopic thermal motion, which results in internal energy losses
A damping parameter takes into account the rate of energy transfer
precession
Landau and Lifshitz, Phy. Z. Sowjet. 8, 101 (1935)

## Slide 5: Magnetization dynamics Landau-Lifshitz-Gilbert (LLG) equation
LL
damping
In standard form
LL cannot account for large damping in thin Permalloy sheets, adjusted by Gilbert
damping
LLG
LLG
LL
Gilbert, IEEE Trans. Magn. 40, 3443 (2004)
Notes: Landau and Lifshitz formulated the theory of dynamics of magnetization in ferromagnetic bodies