## Slide 1: Energy-Efficient Neuromorphic Computing
MS Project: Mid-Term Presentation
Khritish Kumar Behera
Roll: 17125, Email: khritish17@iiserb.ac.in
Electrical Engineering and Computer Science [EECS] Dept.
Indian Institute of Science Education and Research [IISER] Bhopal
Advisor: Dr. Kuntal Roy, Email: kuntal@iiserb.ac.in

## Slide 2: Content
Introduction to Artificial Neural Network:
  Training and Testing Phases
  Perceptron, Activation Function
  Forward Propagation
  Gradient Descent
  Backpropagation
  MATLAB 7x5 Character Recognition
Neural Network using Spintronics:
  Magnetic Anisotropy
  Potential Landscape of a magnet
  Magnetic Field applied in the Hard and Easy Axis
  Multiferroics
  Design of Neural Network in Hardware
Experimental
  Electromagnet
  Magnetic Thermal Annealing
  Gaussmeter

## Slide 3
Spintronics based devices has inherent advantage over transistor:
  Weight, Sum and Threshold function
  Non-volatile in nature
In terms of Energy dissipation, Transistor have ohmic loss, while spintronics devices does not have ohmic loss
Piezoelectric
.
.
x1
x2
xn
Majority of the Neuromorphic Computing are done on transistor based devices
Non-Boolean Computing
Magnetostrictive
Insulator
Write
ReadMTJ

## Slide 4: Artificial Neural Network: Motivation
Why Neural Network ?
Object Detection and Object Identification [1]
Face Recognition [2]
Rise of Self Driving Car (Tesla)
Face Recognition in Airports
Face detection

## Slide 5: Artificial Neural Network: Training & Testing Phase
Neural Network is a two-phase process
Training Phase
Testing Phase
Training Phase:
The model learns the underlying feature and mapping function of the given input-output data
Input data is feed into the model
The model gives some output form which the error is calculated
Based on the error, the tunning parameter of the model is changed
Training Data:
( X , T )
X: Input to the model
T: Expected value for input X
Testing Phase:
Once the modeled is trained, new input data are feed into the model which were never used in the training phase
Testing is also used for checking whether the model is generalizing the data or its more biased towards the trained data
X
O
ERROR: T - O

## Slide 6: Artificial Neural Network: Example
.
.
.
.
.
.
A
4x4 Character Recognition Model:
Each pixel value (1 or 0) is given to the model as input
The model trains on the training data
Later when test data is given, it gives an accurate result

## Slide 7: Artificial Neural Network: Perceptron
X1
X2
X3
W1
W2
W3
∑
σ
b
Y
A Simple Perceptron can have more than one input, but the output needs to be just one
Each input edge has a weight associated with it, which can be negative / positive / zero
Each node has a ‘bias’ term associated with it
The Neuron Process through two sequential processes: Summation and Activation
Perceptron is the simplest and most basic form of a neural network

## Slide 8: Artificial Neural Network: Perceptron
X1
X2
X3
W1
W2
W3
∑
σ
b
Y
1. Weighted Input:
2. Summation of weighted Input
3. Addition of Bias term to the weighted sum
4. Apply Activation form

## Slide 9: Artificial Neural Network: Activation Function
Activation Function is a non-linear mathematical equation
The bias term serves as a threshold value for the activation term:
Activation Function is inspired from biological neuron:
Neurons would not fire and pass the input signal to the next neuron until and unless certain threshold is reached
Bias

## Slide 10: Artificial Neural Network: Activation Function
Non-Linearity of Activation Function is the super-power of Artificial Neural Network
The Yellow circle and the red square are linearly classifiable
The Yellow circle and the red square are not linearly classifiable
Input
Input
Output
Output

## Slide 11: Artificial Neural Network: Activation Function
Rectilinear Unit Function (ReLu)

## Slide 12: Artificial Neural Network: Simple ANN
An Artificial Neural Network is a system of connected artificial neurons
Output of each neuron of one layer is connected to the all of the neurons in the next layer
There are no self loops, no feedback loops
More than one edge emerging out of a neuron, does not mean that there are multiple output of the neuron

## Slide 13: Artificial Neural Network: Simple ANN
Input Layer:
Original Input is given here
Neurons simply transfer the input data to next layer without altering the data
No. of neuron depends on the problem requirement
Hidden Layer:
Neurons in the hidden layer alters the input data
At least one hidden layer is required
At least one hidden neuron is required per hidden layer
Hidden Layer:
Neurons in the hidden layer alters the input data
At least one hidden layer is required
At least one hidden neuron is required per hidden layer

## Slide 14: Artificial Neural Network: Forward Propagation
1
2
3
3

## Slide 15: Artificial Neural Network: Gradient Descent
Error
K (Optimizing Parameter)
Initial Point
LR : Learning Rate

## Slide 16: Artificial Neural Network: Gradient Descent
Error
K (Optimizing Parameter)
The Optimizing parameter is always chosen randomly so as to increase the odd of not getting stuck in a local minima
The problem of getting stuck in a local minima is un-avoidable but it can be minimized

## Slide 17: Artificial Neural Network: Backpropagation
1
2
3
Target

## Slide 18: Artificial Neural Network: Backpropagation
1
2
3
Error

## Slide 19: Artificial Neural Network: Character Recognition
A
A
We wish to create an ANN which can recognize alphabets from a noisy 7x5 pixel binary pattern

## Slide 20: Artificial Neural Network: Character Recognition
Input:
35 Pixel values of the test character
Output:
26 bit array suggesting the character
A: 1,0,0,0,0,0,0,0,…..0,0,0,0
B: 0,1,0,0,0,0,0,0,……0,0,0,0
C: 0,0,1,0,0,0,0,0,……0,0,0,0
Similarly others

## Slide 21: Artificial Neural Network: Character Recognition

## Slide 22: Artificial Neural Network: Character Recognition

## Slide 23: Artificial Neural Network: Character Recognition

## Slide 24: Content
Introduction to Artificial Neural Network:
  Training and Testing Phases
  Perceptron, Activation Function
  Forward Propagation
  Gradient Descent
  Backpropagation
  MATLAB 7x5 Character Recognition
Neural Network using Spintronics:
  Magnetic Anisotropy
  Potential Landscape of a magnet
  Magnetic Field applied in the Hard and Easy Axis
  Multiferroics
  Design of Neural Network in Hardware
Experimental
  Electromagnet
  Magnetic Thermal Annealing
  Gaussmeter

## Slide 25: Spintronics: Spin-Electronics
Electron
Apart from having charge, electron also has a spin
Spin Up (↑) / Down (↓)
Spintronics device are non-volatile and endurable
Which gives an advantage over transistor, since transistor requires extra circuitry to have the non-volatile nature
There is no charge movement, only spin rotation
No ohmic energy dissipation , the only dissipation happens due to damping
Charge
Spin
0 / 1
Spin

## Slide 26: Magnetic Anisotropy
30-80 KT at 300 K
z
y
Magnetization
x
In-plane
Shape anisotropy
CoFeB
M
H
Hk
Ellipsoid
Sphere

## Slide 27: Potential Landscape of Magnet

## Slide 28: Magnetic Field applied on hard axis

## Slide 29: Magnetic Field applied on Easy axis

## Slide 30: Multiferroics
E
P
H
M
E, H
P, M
Ferroelectric
Ferromagnetic
Multiferroic
and magnetoelectric
P
E
H
M
Piezoelectricity
Magnetostriction
Magnetoelectricity (intrinsic)
Multiferroic

## Slide 31: Design of Neural Network
Magnetostrictive
Insulator
Write
ReadMTJ
Piezoelectric
.
.
x1
x2
xn
x1
x2
xn
.
.
.
w1
w2
wn
y = f(u)
f
Neuron
Neural network

## Slide 32: Content
Introduction to Artificial Neural Network:
  Training and Testing Phases
  Perceptron, Activation Function
  Forward Propagation
  Gradient Descent
  Backpropagation
  MATLAB 7x5 Character Recognition
Neural Network using Spintronics:
  Magnetic Anisotropy
  Potential Landscape of a magnet
  Magnetic Field applied in the Hard and Easy Axis
  Multiferroics
  Design of Neural Network in Hardware
Experimental
  Electromagnet
  Magnetic Thermal Annealing
  Gaussmeter

## Slide 33: Experimental
Electromagnet for magnetic alignment
Magnetic Thermal Annealing for better magnetic characterization
Gaussmeter for measuring the magnetic field
Sputtering for deposition of different materials, e.g., piezoelectric, magnets
Electron Beam Lithography (EBL) for patterning single-domain nanomagnets
Magnetic Force Microscopy (MFM) for visualizing single-domain nanomagnets
Ferromagnetic Resonance (FMR) for characterizing the magnetic damping parameter
Vibrating Sample Magnetometer (VSM) for magnetic hysteresis

## Slide 34: Experimental: Electromagnet
Magnetic Coil
Constant Current Power Supply (CCPS)
Gauss Probe
CCPS : Provides Constant Current to the magnetic coils which in turn generates the magnetic field
Gauss Probe: Is used to measure the magnetic field generated at the pole

## Slide 35: Experimental: Magnetic Thermal Annealing
Lattice deformities can degrade material quality
It helps to eliminate structural imperfections
Reorientation of the easy axis in a ferromagnetic material
It reorients each spin along applied magnetic field, if the sample has deformed ferromagnetic lattice

## Slide 36: Experimental: Gaussmeter
Gaussmeter is a static electronic magnetic field measurement device
The Gaussmeter has two probes:
Axial Probe: Which measures the magnetic field parallel to the probe
Transversal Probe: Which measures the magnetic field perpendicular to the probe
It measures by the Hall effect, which is the conversion of magnetic field into Hall Voltage
Electrons in magnetic field tries to move in perpendicular direction of applied magnetic field (Lorentz force)