## Slide 1: Energy-Efficient Neuromorphic Computing
MS Project: Mid-Term Presentation
Khritish Kumar Behera
Roll: 17125, Email: khritish17@iiserb.ac.in
Electrical Engineering and Computer Science [EECS] Dept.
Indian Institute of Science Education and Research [IISER] Bhopal
Advisor: Dr. Kuntal Roy, Email: kuntal@iiserb.ac.in

## Slide 2: Content
Introduction to Artificial Neural Networks
Training and Testing Phase
Perceptron, Activation Function
Forward Propagation
Gradient Descent, Backpropagation
7x5 Character Recognition Model
Neural Network Using Spintronics
Magnetic Anisotropy
Potential Landscape of a Magnet
Magnetic Field applied in the Hard axis and Easy axis
Multiferroics
Design of Neural Network in Hardware
Experimental
Electromagnet
Magnetic Thermal annealing
Gaussmeter
Summary

## Slide 3: Content
Introduction to Artificial Neural Networks
Training and Testing Phase
Perceptron, Activation Function
Forward Propagation
Gradient Descent, Backpropagation
7x5 Character Recognition Model
Neural Network Using Spintronics
Magnetic Anisotropy
Potential Landscape of a Magnet
Magnetic Field applied in the Hard axis and Easy axis
Multiferroics
Design of Neural Network in Hardware
Experimental
Electromagnet
Magnetic Thermal annealing
Gaussmeter
Summary

## Slide 4: Energy-Efficient Neuromorphic Computing
Spintronics based devices has inherent advantage over transistor:
Weight, Sum and Threshold function
Non-volatile in nature
In terms of Energy dissipation, Transistor have ohmic loss, while spintronics devices does not have ohmic loss
Piezoelectric
.
.
Majority of the Neuromorphic Computing are done on transistor based devices
Non-Boolean Computing
Magnetostrictive
Insulator
Write
ReadMTJ
Y
.
.
.
Neuron

## Slide 5: Artificial Neural Network: Motivation
Why Neural Network ?
Object Detection and Object Identification
Face Recognition
Rise of Self Driving Car (Tesla)
Face Recognition in Airports
Face detection
Notes: Talk on success of ANN

## Slide 6: Artificial Neural Network: Training & Testing Phase
Neural Network is a two-phase process
Training Phase
Testing Phase
Training Phase:
The model learns the underlying feature and mapping function of the given input-output data
Input data is feed into the model
The model gives some output, form which the error is calculated
Based on the error, the tunning parameter of the model is changed
Training Data:
( X , T )
X: Input to the model
T: Expected value for input X
Testing Phase:
Once the modeled is trained, new input data are feed into the model which were never used in the training phase
Testing is also used for checking whether the model is generalizing the data or its more biased towards the trained data
X
O
ERROR: T - O

## Slide 7: Artificial Neural Network: Example
.
.
.
.
.
.
A
4x4 Character Recognition Model:
Each pixel value (1 or 0) is given to the model as input
The model trains on the training data
Later when test data is given, it gives an accurate result

## Slide 8: Artificial Neural Network: Perceptron
X1
X2
X3
W1
W2
W3
∑
σ
b
Y
A Simple Perceptron can have more than one input, but the output needs to be just one
Each input edge has a weight associated with it, which can be negative / positive / zero
Each node has a ‘bias’ term associated with it
The Neuron Process through two sequential processes: Summation and Activation
Perceptron is the simplest and most basic form of a neural network

## Slide 9: Artificial Neural Network: Perceptron
X1
X2
X3
W1
W2
W3
∑
σ
b
Y
1. Weighted Input:
2. Summation of weighted Input
3. Addition of Bias term to the weighted sum
4. Apply Activation form

## Slide 10: Artificial Neural Network: Activation Function
Activation Function is a non-linear mathematical function
Bias term serves as a threshold for the activation term:
Activation Function is inspired from biological neuron:
Neurons would not fire, and pass the input signal to the next neuron until and unless certain threshold is reached
Bias

## Slide 11: Artificial Neural Network: Activation Function
Non-Linearity of Activation Function is the super-power of Artificial Neural Network
The Yellow circle and the red square are linearly classifiable
The Yellow circle and the red square are not linearly classifiable
Input
Input
Output
Output

## Slide 12: Artificial Neural Network: Activation Function
Rectilinear Unit Function (ReLu)

## Slide 13: Artificial Neural Network: Simple ANN
An Artificial Neural Network is a system of connected artificial neurons
Output of each neuron of one layer is connected to the all the other neurons in the next layer
There are no self loops, no feedback loops
More than one edge emerging out of a neuron, does not mean that there are multiple output of the neuron

## Slide 14: Artificial Neural Network: Simple ANN
Input Layer:
Simply transfer the input to next layer without altering
No. of neuron based on the problem
Hidden Layer:
At least one hidden layer
At least one hidden neuron per hidden layer
Output Layer:
Final output to the user
No. of neuron based on the problem

## Slide 15: Artificial Neural Network: Forward Propagation
1
2
3
3
Input traversal from Input layer to Output layer through hidden layer

## Slide 16: Artificial Neural Network: Gradient Descent
Error
K (Optimizing Parameter)
Initial Point
LR : Learning Rate

## Slide 17: Artificial Neural Network: Gradient Descent
Error
K (Optimizing Parameter)
K is chosen randomly to increase the probability to not get stuck in a local minima
Getting stuck in local minima is un-avoidable but can be minimized

## Slide 18: Artificial Neural Network: Backpropagation
1
2
3
Target

## Slide 19: Artificial Neural Network: Backpropagation
1
2
3
Error

## Slide 20: Artificial Neural Network: Character Recognition
A
A
We wish to create an ANN which can recognize alphabets from a noisy 7x5 pixel binary pattern

## Slide 21: Artificial Neural Network: Neural Architecture
Input:
35-Bit word of the test character
Output:
26-Bit word suggesting the character
A: 1,0,0,0,0,0,0,0,…..0,0,0,0
B: 0,1,0,0,0,0,0,0,……0,0,0,0
C: 0,0,1,0,0,0,0,0,……0,0,0,0
Similarly others

## Slide 22: Artificial Neural Network: Setting Neural Architecture
No. of Hidden Layer ?
Error
Neurons no.
Testing Error
Training Error
Optimal number of neurons in hidden layer
Error Gap:
(Testing Error – Training Error)
at the optimal hidden neuron
Error Gap
No. of Hidden Neuron per Hidden Layer ?
Optimal number of neuron for a hidden layer:
Plot the testing and training error iterating from 1 to Max hidden neuron
Consider those neuron where testing error has minima
Optimal number of hidden layer:
Calculate the no. of hidden neuron for first layer
Using this no. calculate for second layer, continue until the error gap starts increasing

## Slide 23: Artificial Neural Network: Noise Tolerance
Test Data with mix noises varying from 4-bit to 8-bit Results:
Correct Prob. = 0.7203
Wrong Prob. = 0.2797
Noise tolerance is up to 6-Bit flip
520 data of these 26 character were taken and added some noise degree ranging from 4-Bit to 8-Bit flip
4-Bit Flip
Correct Recognition: 0.913
Wrong Recognition: 0.087
5-Bit Flip
Correct Recognition: 0.7942
Wrong Recognition: 0.2058
6-Bit Flip
Correct Recognition: 0.7077
Wrong Recognition: 0.2923
7-Bit Flip
Correct Recognition: 0.5923
Wrong Recognition: 0.4077
8-Bit Flip
Correct Recognition: 0.4635
Wrong Recognition: 0.5365

## Slide 24: Artificial Neural Network: Noise Tolerance
4 BIT FLIP
5 BIT FLIP
6 BIT FLIP
7 BIT FLIP
8 BIT FLIP
A
A
G
Q
A
ORIGINAL



## Slide 25: Content
Introduction to Artificial Neural Network
Training and Testing Phase
Perceptron, Activation Function
Forward Propagation
Gradient Descent, Backpropagation
7x5 Character Recognition Model
Neural Network Using Spintronics
Magnetic Anisotropy
Potential Landscape of a Magnet
Magnetic Field applied in the Hard axis and Easy axis
Multiferroics
Design of Neural Network in Hardware
Experimental
Electromagnet
Magnetic Thermal annealing
Gaussmeter
Summary

## Slide 26: Spintronics: Spin-Electronics
Electron
Along with charge, electron have a spin
Spin Up (↑) / Down (↓)
Spintronics device are non-volatile and endurable
Which gives an advantage over transistor, since transistor requires extra circuitry to have the non-volatile nature
There is no charge movement, only spin rotation
No ohmic energy dissipation , the only dissipation happens due to damping
Charge
Spin
0 / 1
Spin

## Slide 27: Magnetic Anisotropy
30-80 KT at 300 K
z
y
Magnetization
x
In-plane
Shape anisotropy
CoFeB
M
H
Hk
Ellipsoid
Sphere

## Slide 28: Potential Landscape of Magnet
Notes: Increase the axis font, plot phi 85-95

## Slide 29: Magnetic Field applied along in-plane hard axis
Magnetic Field applied along Y-axis
Notes: Plot it, animation with magnetization direction

## Slide 30: Magnetic Field applied along in-plane Easy axis
Magnetic Field applied along Z-axis
Notes: Plot it, animation with magnetization direction

## Slide 31: Magnetic Field applied along in-plane hard axis
Magnetic Field applied along Y-axis
Notes: Plot it, animation with magnetization direction

## Slide 32: Magnetic Field applied along in-plane Easy axis
Magnetic Field applied along Z-axis
Notes: Plot it, animation with magnetization direction

## Slide 33: Multiferroics and Multiferroic Composites
Piezoelectric
Strain
Magnetostrictive
P
E
H
M
Piezoelectricity
Magnetostriction
Magnetoelectricity (intrinsic)
P
E
H
M
Piezoelectricity
Magnetostriction
Magnetoelectricity (intrinsic)
Multiferroic
Notes: Change it to multiferroic composites

## Slide 34: Magnetostriction
Magnetostrictive Material : Certain ferromagnetic specimen changes its shape (strain: ) during the process of magnetization
Magnetostriction Co-efficient
Magnetostrictive Anisotropy ↔ Stress Anisotropy
Cobalt:
FeGa:
Stress Anisotropy (for FeGa):
(max.)
Notes: 40KT =1eV=1.610-19J

## Slide 35: Multiferroic composites Voltage vs stress anisotropy
Vin
tpiezo
Y: Young’s modulus
strain transfer
Piezoelectric
Magnetostrictive
z (3)
x (1)
tmag
y (2)
magnetostrictive layer
with high
Choose piezoelectric layer with high de-coefficient

## Slide 36: Multiferroic composites Voltage vs stress anisotropy
Vin
tpiezo
Y: Young’s modulus
tpiezo should be high enough for assumption
strain transfer
Piezoelectric
Magnetostrictive
z (3)
x (1)
tmag
Anisotropic strain along the two directions of lateral area (PMN-PT, PZN-PT)
y (2)
magnetostrictive layer
with high (3/2)sY/(1+)
(e.g., Terfenol-D, Galfenol)
Choose piezoelectric layer with high d31- d32 (e.g., PMN-PT, PZN-PT)
: Poisson’s ratio

## Slide 37: Design of Neural Network
Magnetostrictive
Insulator
Write
ReadMTJ
Piezoelectric
.
.
x1
x2
xn
Neuron
Electric Potential
Stress in Piezoelectric
Stress in Magnetostrictive
Changes magnetization of Magnetostrictive
Changes the magnetization direction in the lower plate of TMR
Creates different resistance
.
.
.

## Slide 38: Content
Introduction to Artificial Neural Network
Training and Testing Phase
Perceptron, Activation Function
Forward Propagation
Gradient Descent, Backpropagation
7x5 Character Recognition Model
Neural Network Using Spintronics
Magnetic Anisotropy
Potential Landscape of a Magnet
Magnetic Field applied in the Hard axis and Easy axis
Multiferroics
Design of Neural Network in Hardware
Experimental
Electromagnet
Magnetic Thermal annealing
Gaussmeter
Summary

## Slide 39: Experimental
Electromagnet for magnetic alignment
Magnetic Thermal Annealing for better magnetic characterization
Gaussmeter for measuring the magnetic field
Sputtering for deposition of different materials, e.g., piezoelectric, magnets
Electron Beam Lithography (EBL) for patterning single-domain nanomagnets
Magnetic Force Microscopy (MFM) for visualizing single-domain nanomagnets
Ferromagnetic Resonance (FMR) for characterizing the magnetic damping parameter
Vibrating Sample Magnetometer (VSM) for magnetic hysteresis

## Slide 40: Electromagnet
Constant Current
Power Supply
Magnetic Coil
Gauss Probe
Chiller
Magnetic Coil: When electric current is passed through the magnetic coils it generates a constant magnetic field
Gauss Probe: It is used to measure the magnetic field generated between the poles
Constant Current Power Supply: Provides a constant current to the magnetic coil which in turn a constant magnetic field
Chiller: Is required to reduces the temperature of the magnetic coil

## Slide 41: Magnetic Thermal Annealing
Reorients the spin direction in the direction of the magnetic field
Enhances the magnetic property of magnetic materials
Heater
Vacuum Pump
Heating of the sample is done in vacuum and the material MTA is made up of is not affected by the magnetic field

## Slide 42: Gaussmeter
Gaussmeter is a static electronic magnetic field measurement device
Probes used in Gaussmeter:
Axial Probe: Measures the magnetic field parallel to the probe
Transversal Probe: Measures the magnetic field perpendicular to the probe
It measures by the Hall effect, which is the conversion of magnetic field into Hall Voltage
Electrons in magnetic field tries to move in perpendicular direction of applied magnetic field (Lorentz force)
Gauss Probe

## Slide 43: Gaussmeter
R = 2.5cm :
R = 3.6cm :
R = 5cm :
H↑
H↑
H↑

## Slide 44: Gaussmeter
R = 2.5cm :
R = 3.6cm :
R = 5cm :
H↑
H↑
H↑
→
→
→

## Slide 45: Summary
Understanding of the working principle of ANN
Implemented a 7x5 Character Recognition Model
Learned about magnetic anisotropy, Multiferroics and Multiferroic Composites
Implemented the above learned concepts in sketching out the idea for making a hardware based artificial neuron
Worked on EM, ETA and Gaussmeter
Future Works
Will start working on sputtering for deposition, EBL for pattering
Fabrication of the device
Notes: Write in the perspective of what I have done until now and what I will do in the project